## Slide 1: Training 1: Architecture and abstraction layers
Part of cooperative research platform (CRP) project between SZE and Bosch.

## Slide 2: Agenda
Training 1: Architecture and abstraction layers
Motivation
Definitions – common language
Top-down: architecture concepts
Example: CRP at Lexus and Leaf
Proper documentation
Repository structure
Responsibilities

## Slide 3: Motivation
Training 1: Architecture and abstraction layers
„Let’s develop a function!”
„Ok, what shall it do?”
„It shall keep the vehicle in the lane.”
„Ok, what measures the lane?”
„It’s from a Lidar. It detects the lane by having a pointcloud based algorithm.”
„Cool! Let’s do it!”
<3 weeks later>
„We need to bring the Lexus back… Please use the Leaf instead…”
<1 day later>
„Ok, we took the Leaf out, run the exact same software, but nothing happened… The lanes were not detected at all… Still, we have Lidar on it…”
„But what kind of lidar? Is it the same as on the Lexus?”
„No, it’s a different kind, with different driver…”

## Slide 4: Motivation
Training 1: Architecture and abstraction layers
Now what? Different lidar, different driver…
Option 1:
  „Let’s adjust the code to use the other lidar”
  „But it’ll take a lot-of-time…”
  „Why?”
  „Because the driver is integrated to the detection node, so the whole detection node code shall be overwritten…”
  „…”
  <6 weeks later>
  „Ok, Lexus is back. But somehow the code is not the same, so it won’t run…”
  …
Now what? Different lidar, different driver…
Option 2:
  „It’s ok, the detection code is the same, the provider of the point cloud topic is different. Only the adapter node shall be changed.”
  „Ok, it’s not a big issue.”
  „Please also add a configuration parameter for the vehicle”
  <6 weeks later>
  „ Ok, Lexus is back. I changed the vehicle parameter and it runs again!”
  „But there were changes in the function!”
  „Yes, but it’s nothing to do with the vehicle!”

## Slide 5: Motivation
Training 1: Architecture and abstraction layers
Further examples:
  ROS1 vs ROS2 vs any other platform
  Simulation vs Vehicle…
Statements:
It is not enough to keep the concept in head.
An architecture must be defined that implicitely supports the layer configuration as well as the vehicle variants.
For that, common definitions shall be used.
Also, the documentation shall reflect to the concept itself.

## Slide 6: Definitions – common language
Training 1: Architecture and abstraction layers
Function development: the exact algorithm and what is behind, usually managed by experts on a given field.
Architecture development: relations between components (e.g., software architecture) or devices (system architecture). Higher level knowledge of the entire function.
Integration: persons who put the different components together to form an entire (E2E) function.
Vehicle integration layer: to put and E2E software function into a vehicle, and let is be an E2E system function.
Controller integration layer: on a given HW (ECU,PC) the software shall run. It takes connection to outer world as well as internal (application) layer(s).
Application layer: the place of the software functions by ensuring it receives/sends the right information to other functions or the outer world.
Function layer: no HW, no MW relations, only SW functions (e.g., no ROS dependencies).

## Slide 7: Top-down: architecture concepts
Vehicle integration layer
Training 1: Architecture and abstraction layers
Controller integration layer
(~MW-ROS)
Functional Layer
Application layer
(MW-ROS)
CAN driver
Sensor driver 1
Sensor driver 2
Sensor abstraction
Topic handler
Function Code
Configuration
Topic handler
Actuator abstraction
CAN driver

## Slide 8: Top-down: architecture concepts
Training 1: Architecture and abstraction layers
Drivers: connects the specific interface of the given data provider (e.g., sensor, map service, external interface…etc.) and translates it to a message format that is readable by the controller integration layer. In the case of a Linux PC and ROS, this means e.g., CAN message  ROS topic translation. The drivers can provide data in any form that is the easiest by the device.
Sensor abstraction: dual task
  1. Translates different sensor data (e.g., different LiDARs) to one specific format (e.g., pointcloud2D, in given frame, with given resolution…etc.) that is automatically readable by the application layer. The goal is that without modifying the application layer sensors can be changed  algorithms can be changed.
  2. Different vehicle configuration can be switched.
Actuator abstraction:
  Translate vehicle-level target values to actuator targets (e.g., longitudinal acceleration to brake and engine target values)

## Slide 9: Top-down: architecture concepts, Function code vs. Application layer
Training 1: Architecture and abstraction layers
In the function, define your own interfaces, that lack any middle-ware (i.e., ROS) types!
Example: https://github.com/szenergy/autonomous_master_repo/blob/release_auc2023/src/trajectory_planner/src/trajectoryPlannerRunnable.cpp
„runnable.cpp” contains the node definition, mapping the topics to internal types.
Therefore, function code can be relocated to other middleware systems.
  Or can be used in simulation
Application layer
(MW-ROS)
Topic handler
Function Code
Topic handler

## Slide 10: Proper documentation
Training 1: Architecture and abstraction layers
Let’s support one-document concept: a big document that contains all discussion layers
  Store document in the repository ~ part of product
Requirements: let’s follow V-model! (topic of the next training)
Be consistent in naming convention and definitions
Comments in code  readable by everyone
Pull requests and branching culture:
  Keep the level of branches low (e.g., one main branch, and one side branch, no more levels)
  Open PR when somebody who is not fully involved develops somethings
Continuous testing:
  Always test everything works before merging it to main branch
  How can we define ‚it works’? Integration team: test E2E regularly, even with the tiniest modifications to track errors in time.

## Slide 11: Continuous testing
Training 1: Architecture and abstraction layers
Test catalogue: simple list of test cases to run regularly
Test reporting: way of storing results and track software versions under test  tags in github?
What is the right frequency of testing?
What is the right test catalogue  functions and scenarios define.
Always iterate and fix problems that are revealed  continuous development.

## Slide 12: Repository structure
Training 1: Architecture and abstraction layers
Root folder/
crp_APL (includes crp_FUL, structure defined by MW, e.g., ROS)
  function1_apl (may be a subrepo)
    src_ful (does not contain mw dependencies)
              src
              Inc
              doc
    src
    inc (includes src_ful files)
    …
  function2_apl
  …
crp_CIL (includes crp_APL)
crp_VIL (includes crp_CIL)
tools
doc
Risk: how can define this as a proper workspace?
ros2_ws/src/<repo_root>/crp_apl/function_apl/src
Note: at the apl level standalone features can be kept. But at higher level, e.g., CIL/VIL this is not a must. But: codes that relate to e.g., VIL features can be included simply in VIL/CIL folders.

## Slide 13: Repository structure - Autoware
Training 1: Architecture and abstraction layers
Autoware will serve as a third-party product.
It needs special care (e.g., own workspace) to work properly. Therefore its integration to the crp repo is not recommended.
Dependencies are handled at CIL level  e.g., launch file defines the applications to run.
Autoware is located in a different folder.

## Slide 14: Responsibilities
Training 1: Architecture and abstraction layers
Research Integration Team
  Provides capability of testing E2E functions
  Knowledge in vehicle integration, communication, middleware
  Calibration and application of ideas
  They are responsible for building and maintaining the Corporate Research Platform.
Function Research Team
  Function research and development, esp. active in the function code level
  They have detailed knowledge in their own field, develop functions knowing what the system is capable of.
  They develop new ideas, as part of their research.
Software Architect Team
  Mainly collection of members of the previous two who have wide overview on all topics
  Additional members of the research team
  This team defines what should be developed on function and architecture-wise